## Slide 1: Type qualifiers

## Slide 2: C – type qualifiers
The keywords which are used to modify the properties of a variable are called type qualifiers.
There are three types of qualifiers available in C language. They are,
const
volatile
restrict

## Slide 3: Const
Constants are also like normal variables. But, only difference is, their values can’t be modified by the program once they are defined.
They refer to fixed values. They are also called as literals.
They may be belonging to any of the data type.
Syntax: const data_type variable_name; (or)
const data_type *variable_name;

## Slide 4: Example 1
#include<stdio.h>
void main(){
int a = 10;
const int b = 20 ;
a = 15 ;
b = 25 ; // creates an error
printf(“a = %d\nb = %d", a, b ) ;
}

## Slide 5: Volatile
When a variable is defined as volatile, the program may not change the value of the variable explicitly.
But, these variable values might keep on changing without any explicit assignment by the program. These types of qualifiers are called volatile.
For example, if global variable’s address is passed to clock routine of the operating system to store the system time, the value in this address keep on changing without any assignment by the program. These variables are named as volatile variable.
Syntax: volatile data_type variable_name; (or)
volatile data_type *variable_name;

## Slide 6: volatile
static int WAIT;
void fun(void)
{
WAIT=0;
while (WAIT!=255);
}
void fun_optimized(void)
{
foo=0;
while (true);
}
static volatile int WAIT;
void fun(void)
{
WAIT=0;
while (WAIT!=255);
}

## Slide 7: volatile
The volatile keyword indicates to the compiler, that a variable may be modified outside of the program.
A volatile variable is normally used in multitasking systems, when writing drivers with interrupt service routines, or in embedded system, where the peripheral registers may also be modified by harware device.
Volatile keyword : run slower, program will be larger
Used when a variable is used in various context
Used when common variable is used in more than one task or thread

## Slide 8: restrict
int *ptr
int a= 0;
ptr = &a;
____
____
____
*ptr+=4; // Cannot be replaced with *ptr+=9
____
____
____
*ptr+=5;
restrict int *ptr
int a= 0;
ptr = &a;
____
____
____
*ptr+=4; // Can be replaced with *ptr+=9
____
____
*ptr+=5;
____
____
This is used only with pointers. It indicates that the pointer is only an initial way to access the deference data. It provides more help to the compiler for optimization.